## Slide 1: Car Child Seat Alert System
Presenters: Christopher Atkinson
Prithvi Thimmanayakanahalli Bachireddy

## Slide 2: Overview
Concept
System Design
Design Methodology
Requirements
Module Testing
System Testing and Results
Future Scope
Conclusion

## Slide 3: Concept
Each year, an average of 37 children die in hot cars in the US
Design a system for monitoring a vehicle for a child left alone in a car
Use an embedded system for monitoring
  Connects to software running on PC via Wi-Fi
Utilize a software backend that connects to Amazon Web Services (AWS) Internet of Things (IoT) for communicating with the user
Send an alert via text and email if a child is left alone in a vehicle

## Slide 4: System Design
Child Alert System
Embedded System
IoT Server
Hardware
Software
Sensors
Wireless Hardware
SNS

## Slide 5: Entity Relationship Diagram
Child
Driver
Embedded System
AWS IoT
Sensors
Monitor
Monitor
Communicates with
Alerts

## Slide 6: Hardware Selection
Arduino Nano 33 IoT selected as embedded system processor
  Contains onboard Wi-Fi/Bluetooth module
3-wire strain gauges
  Used in pairs to monitor driver and child
  Generates a voltage differential when force is applied
HX711 ADC board
  Combines strain gauges in Wheatstone bridge
  24-bit ADC communicates with Arduino
  Allows Arduino to read voltage difference from strain gauges

## Slide 7: Detailed System Diagram
Embedded System
PC Console
AWS IoT
AWS SNS
Wi-Fi
SMS
Email

## Slide 8: Data Flow Diagrams
Child Alert System
Sensors
Alert
Input data
Output data
Sensors
Alert
Embedded System
AWS IoT
Send an Alert
Sensor Status
Send an Alert
Level 0
Level 1

## Slide 9: Design Methodology
Project used the Agile methodology throughout development
Project was divided into three phases:
  Identify system and subsystem requirements
    Includes choosing hardware and programming languages
  Subsystem design, implementation, and testing
  System integration and testing
Short weekly meetings held to discuss problems, design, and progress

## Slide 10: Requirements
System Requirements
  [SYSFUNCT001] The system shall consist of hardware and software components that have the capability of monitoring a vehicle for the presence of a driver and child as well as the capability of alerting a user via text or email.
  [SYSFUNCT002] The system shall have a user-configurable delay for signaling an emergency event.
  [SYSPERF001] The system shall alert a user within 30 seconds (1-sigma) of an emergency event.
  [SYSPERF002] The system shall alert a user for the second time with 3 minutes delay if no action is taken for the first alert.

## Slide 11: Requirements
Embedded System Requirements
  [ESFUNCT001] The hardware shall consist of an embedded system with one or more microprocessors, one or more sensors, and the hardware to support a wireless communication method (WI-FI or Bluetooth preferred).
  [ESPERF001] The hardware shall transmit an alert to the backend system within 15 seconds (1-sigma) of an emergency event.

## Slide 12: Requirements
Backend Requirements
  [BEFUNCT001] The software shall receive notifications wirelessly (using WI-FI or Bluetooth) from the hardware and transmit a notification to the user via text message or email.
  [BEFUNCT002] The software shall be written in a high-level programming language such as C++, Java, or a similar language.
  [BEPERF001] The software shall transmit an alert to the user within 15 seconds (1-sigma) of an alert received from the hardware.

## Slide 13: Testing Plan
Testing plan designed for system and subsystem designs
Subsystem modules tested individually before integration to verify requirements compliance and functionality
System then integrated and tested

## Slide 14: Embedded System Testing
Test Case No | Test Objective | Test Procedure | Expected Result | Actual Result | Test Case Result
1 | Test Arduino WiFi connection | 1. Program Arduino with code that connects to a WiFi connection 2. Print a SSID of the network and the IP address of the Arduino to a serial output | Printed lines to serial monitor that display the SSID of the network and the IP address assigned | Arduino successfully connects and transmits the SSID and ssigned IP address | Pass
2 | Test Driver strain gauge configuration | 1. Wire strain gauges together 2. Connect strain gauges to HX711 3. Connect HX711 to power 4. Apply pressure to strain gauges and monitor the A+ and A- pins for voltage differences with a voltmeter | Extremely small voltage differential will be visible on a voltmeter | Voltage differential of 3-8 mv | Pass
3 | Test Child strain gauge configuration | 1. Wire strain gauges together 2. Connect strain gauges to HX711 3. Connect HX711 to power 4. Apply pressure to strain gauges and monitor the A+ and A- pins for voltage differences with a voltmeter | Extremely small voltage differential will be visible on a voltmeter | Voltage differential of 3-8 mv | Pass
4 | Test Driver HX711 configuration | 1. Connect strain gauges to HX711 2. Connect HX711 to Arduino 3. Program Arduino with a program to read the HX711 | Serial readout of strain gauge force. Result will initially be uncalibrated so may be unusual | Displayed rresulting force in KG. Calibration factor of 7050 chosen to zero scale | Pass
5 | Test Child HX711 configuration | 1. Connect strain gauges to HX711 2. Connect HX711 to Arduino 3. Program Arduino with a program to read the HX711 | Serial readout of strain gauge force. Result will initially be uncalibrated so may be unusual | Displayed rresulting force in KG. Calibration factor of -7050 chosen to zero scale | Pass
6 | Test alert generation code | 1. Apply weight to both strain gauges 2. Remove weight from driver gauge for more than 30 seconds | Serial readout will display a message that a child has been left alone in the car | Received a message on serial readout that a child was alone in the car | Pass

## Slide 15: Backend System Testing
Test Case No | Test Objective | Test Procedure | Expected Result | Actual Result | Test Case Result
1 | AWS IOT Topic and Certificate creation ECE574_Project | 1.Create a AWS IOT Account. 2. Register Thing In AWS IOT Console. 3. While Registering Thing,Download Certificates and Keys. 4. Save the Thing ARN for further process. | AWS IOT TOPIC ECE574_Project and Certificate (a407f17540af4eff9cea03e3cc1b63b8555b3bfb90bd61d32311944b8267349b) Should be created and visible in AWS Console. | Certificate visible in AWS Console | Pass
2 | AWS IOT policy creation ECE574_Project | 1. Create Policy in AWS IoT Console 2. Save the Policy ARN. | AWS IoT POLICY ECE574_Policy Should be created and visible in AWS Console | AWS IoT Policy visible in AWS Console | Pass
3 | Attaching the Thing and Policy to Certificates | 1. Open the Generated Certificate in AWS IoT Console. 2. In Actions select Attach Thing. 3.Then again In Actions select Attach Policy | The Policy ECE574_Policy and Thing ECE574_Project should be Attached and visible In the Certificate Console. | Policy and Thing visible in Certificate Console | Pass
4 | Subscribe and Publish a message to the created Topic using AWS MQTT Client | 1. In test Console Enter the Topic ECE574_Project under Subscription Topic. 2. Click on Scbscribe to Topic. 3.Specify a topic and a message to publish with a QoS of 0. 4.Click on Publish to Topic | The Published message should be visible on subscriptions under Thing ECE574_Project. | Published message visible on subscriptions console | Pass
5 | Creation of SNS topic in Amazon SNS | 1. Open Amazon SNS Console. 2. Create a Topic ChildAlertSystem. 3.copy and save the topic ARN | The Topic Child Alert System should be created and visible in Amazon SNS | Child Alert System topic is visible | Pass
6 | Creation of SNS topic Subscription in Amazon SNS | 1.Open the created SNS topic. 2. Click on Create Subscription. 3.Select the Protocol type and enter the endpoint(Mobile Numer). 4.Click on Create Subscription. | The SNS Subscriptions should be created and visible under SNS topic | SNS endpoint subscriptions are visible | Pass
7 | Publishing a message in SNS topic | 1. click on Publish Message. 2.Fill the Message Details and Body and Attributes. 3.Click on publish message. | The Published message should be visible in provided End Point Mobile. | Messages received on mobile devices | 

## Slide 16: System Testing and Results
Procedure
  Weight applied to strain gauges
  Remove weight from driver gauges
Results
  System waits for selected timeframe
  Serial monitor provides warning that driver is absent
  Texts and emails received on both mobile devices
System-level testing was successful

## Slide 17: Conclusion
Developed a child car seat alert system
All requirements successfully met
System monitors seat sensors for a driver and child
Sends text and email alert if child has been left alone in the car